# Repository Information
1. Name
  1. stepper_controller_5x3
2. Version
  1. 1.1
3. License
  1. Open-Source Hardware
4. URL
  1. https://github.com/janelia-kicad/stepper_controller_5x3
5. Author
  1. Peter Polidoro
6. Email
  1. peterpolidoro@gmail.com
## Description
This board controls up to 3 stepper motors with optional forward and reverse limit switches for each motor.
# Images

# Schematic
./schematic/stepper_controller_5x3.pdf

# Gerbers
Send gerbers zip file to your favorite PCB manufacturer for fabrication.
./gerbers/stepper_controller_5x3_v1.1.zip

# Bill of Materials
## PCB Parts
Item	Reference(s)	Quantity	PartNumber	Vendor	Description
1	C1 C12 C19 C26 C4 C5	6	399-13229-1-ND	digikey	CAP CER 0.1UF 100V X7R 1210
2	C10 C11 C15 C16 C17 C18 C22 C23 C24 C25 C8 C9	12	478-1350-1-ND	digikey	CAP CER 470PF 100V X7R 0805
3	C13 C20 C6	3	PCE3812CT-ND	digikey	CAP ALUM 220UF 20% 50V SMD
4	C14 C2 C21 C3 C7	5	445-4536-1-ND	digikey	CAP CER 10UF 50V 10% X7S 1210
5	CLK1	1	CTX277LVCT-ND	digikey	OSC XO 32.000MHZ HCMOS TTL SMD
6	D1	1	568-11697-1-ND	digikey	DIODE SCHOTTKY 45V 10A CFP15
7	L1 L10 L11 L12 L2 L3 L4 L5 L6 L7 L8 L9	12	XC2328CT-ND	digikey	FIXED IND 90NH 8A 8.5 MOHM SMD
8	MDB1	2	S1011E-25-ND	digikey	25 Positions Header Breakaway Connector 0.1in
9	P1	1	CP-063BH-ND	digikey	CONN PWR JACK DC 2.5X5.5 8A T/H
10	R1	1	P1.00KAACT-ND	digikey	RES SMD 1K OHM 1% 1/2W 1210
11	REG1	1	945-1395-5-ND	digikey	CONV DC/DC 1A 5V OUT SIP VERT
12	RV1 RV10 RV11 RV12 RV13 RV14 RV15 RV16 RV17 RV18 RV2 RV3 RV4 RV5 RV6 RV7 RV8 RV9	18	495-7454-1-ND	digikey	VARISTOR 47V 80A 0805
13	SS1 SS2 SS3	48	ED90331-ND	digikey	CONN PIN RCPT .025-.037 SOLDER
14	T1 T3 T5	3	277-1152-ND	digikey	TERM BLOCK HDR 4POS VERT 5.08MM
15	T2 T4 T6	3	277-1223-ND	digikey	TERM BLOCK HDR 4POS VERT 3.81MM
16	U1	1	1460-1071-1-ND	digikey	IC MOTOR CONTROLLER SPI 32QFN
17	U2	1	296-14668-1-ND	digikey	Buffer Non-Inverting 1 Element 8 Bit per Element Push-Pull Output 20-SOIC
18	U3 U4 U5	3	MAX6817EUT+TCT-ND	digikey	IC DEBOUNCER SWITCH DUAL SOT23-6

## Supplemental Parts
Item	Quantity	PartNumber	Vendor	Description
1	3	277-1013-ND	digikey	TERM BLOCK PLUG 4POS STR 5.08MM
2	3	277-1042-ND	digikey	TERM BLOCK PLUG 4POS 5.08MM
3	3	277-1163-ND	digikey	TERM BLOCK PLUG 4POS STR 3.81MM
4	3	277-1193-ND	digikey	TERM BLOCK PLUG 4POS 90DEG 3.81MM
5	3	1460-1187-ND	digikey	TMC2130 STEPPER DRIVER BOARD
6	3	501100B00000G-ND	digikey	HEATSINK 14-DIP/16-DIP
7	1	3M10315-ND	digikey	TAPE ADHESIVE TRANSFER 1/2in X5YD

## Vendor Parts Lists
./bom/digikey_parts.csv
./bom/supplemental_digikey_parts.csv
# Supplemental Documentation
## Assembly Instructions
- Solder header pins into the stepper driver board(s), making note of TOP label. Insert header pins on bottom of board so that the long unsoldered header pins point down when the TOP label faces up.
- Expose one side of the thermal adhesive tape and attach to the bottom of the heatsink. Trim tape so it does not extend beyond heatsink edges.
- Expose the other side of the thermal adhesive tape and attach the heatsink to the stepper driver board on the side with the TOP label.
- Solder surface mount and through hole components onto the pcb.
- Insert stepper driver board(s) into pin receptacles.